Working at Height - Safe use of Ladders

1. Choice of equipment – will be determined by

• the task - height and equipment to be used

• the site conditions and location

• the extent and duration of the work

• the frequency of access required

• risks associated with the task

• number of people required.

• Class 1 or EN131 should be used

For some jobs mobile elevating work

platforms or other work platforms are better

options. Ladders should be used for light, low

hazard work of short duration at lower levels.

2. Common hazards associated with ladder use

• Falls stepping off and on lower rungs

• Ladder slipping sideways at upper resting

point due to overreaching or instability.

• Ladder slipping outwards at the bottom

due to unsuitable ground conditions or

incorrect angle.

• Ladder failure

• Electric shock due to overhead electrical

hazards

• Injury when handling ladders

• Injury to others from falling tools

• Working from too short a ladder.

3. Stability of ladders

• Use on hard, flat, level surface where

possible

• Stabilise by tying to a suitable point to

prevent movement where possible, or use

proprietary stability devices.

• Ensure ladders are fitted with anti-slip feet

• Place ladders at correct angle (75 degrees

or 1m out for every 4 m up).

• Rest the top against a suitable firm surface

(not plastic gutters, glass or infill panels).

• Ensure ladder rungs and stiles are clean

and not slippery

• Ladder accessories may improve stability

and should be used where appropriate,

e.g. stile extensions for stability on slopes.

4. Is the ladder long enough?

• Overall length is not the same as “usable”

length - allow 1 metre of ladder above the

highest rung you use.

• Avoid standing on the top 3 rungs.

• Current best practice is to limit ladder

length to a maximum of 9 metres.

5. Maintenance

• Ladders are “work equipment” and subject

to the requirements of the Provision and

Use of Work Equipment Regulations 1998

• Ladders should be individually identified

and listed on an equipment register which

records: - the make / type / duty / weight /

class rating and date first put into use.

• Ladders should be inspected regularly (at

least 3 monthly) and condition recorded.

• Procedures should be in place for dealing

with defects, which will include repairs or

removal from service

• Ladders should be checked daily before use

for defects – e.g. cracked, bent or warped

stiles; cracked, bent or missing rungs; loose

defective or missing feet, tie rods or

brackets; corrosion of fittings, etc.

6. Ladder safety tips

• Ladders should not be left unattended

• Warning signs should be displayed in public

areas and protection from traffic is essential

• Personal tools and equipment should be

secured at all times when going up and

down ladders, i.e. use tools belts or carriers

• Never use a painted ladders – the paint may

be hiding defects.

• Check for overhead electricity lines before

putting up the ladder.

• Get help to carry heavy ladders.

• Footing will not prevent sideways slip at

top of ladders.

• Use barriers to prevent people walking

beneath them.

• Ensure all users are aware of the points in

this document.

7. Stepladder safety (as above plus)

• Anti-slip feet should be present, in good

repair and clean.

• Check they are sturdy and stable prior to

use - do not use if unstable.

• Only use when they are the most suitable

means of access.

• Avoid using on packaging, soft or sloping

ground, or slippery surfaces.

• Use with the steps facing the work activity

to avoid imposing a side loading, unless no

side load or to improve access to the task.